## Slide 1: Subject: Multimedia Computing and Technology CHAPTER-4 Video and Animation
By: Ramesh Basaula

## Slide 2: Video
Both video and animation give us a sense of motion.
They exploit some properties of human eye’s ability of viewing pictures.
Motion video is the element of multimedia that can hold the interest of viewers in a presentation.
Videos are the visual multimedia source that combines a sequence of images to form a moving picture.
Video usually have audio components that corresponds with the pictures being shown on the screen.

## Slide 3: Visual Signal Representation
In conventional black and white TV sets, the video signal is displayed using a CRT.
An electron beam carries corresponding pattern information, such as intensity in a viewed scene.
Video signal representation includes three aspects:
  The Visual Representation
  Transmission and
  Digitization

## Slide 4: A) Visual Representation
The main objective of visual representation is to offer the viewer as a sense of presence in the scene and of particular in the events portrayed.
To meet this objective, the televised image should convey spatial and temporal content of the scene.
Important aspects of Visual Representation are –
  Visual Detail and Viewing Distance
  Horizontal Detail and Picture Width
  Total Detail Content of the image
  Perception of Depth
  Luminance and Chrominance
  Temporal Aspects of Illuminance
  Continuity of Motion
  Flicker
  Temporal Aspect of Video Bandwidth

## Slide 5
(1) Visual Detail and Viewing Distance:
  The geometry of a TV image is based on the ratio of the picture width W to height H. It is called aspect ratio.
(2) Horizontal Detail and Picture Width:
  The picture width chosen for conventional TV service is 4/3 x picture height.
  The horizontal field of view from the horizontal angle can determine using aspect ratio.
(3) Total Detail Content of the image:
  The vertical resolution is equal to the number of picture elements separately presented in the picture height, while the number of elements in the picture width is equal to the horizontal resolution times the aspect ratio.
  the total number of picture elements (pixel) in the image = number of pixels placed vertically * number of pixels placed horizontally
(4) Perception of Depth:
  In natural vision, perception of the third spatial dimension, depth, depends primarily on the angular separation of the images received by the two eyes of the viewer.
  The choice of the focal length of lenses and changes in depth of focus in camera influence the depth perception.

## Slide 6
(5) Luminance and Chrominance:
  Luminance: The intensity of light emitted from a surface per unit area in a given direction. (represents brightness)
  The brightness of light is measured in terms of Luminance.
  Chrominance: It is the signal used in video system to convey the color information of the picture. (refers to the colour information).
(6) Temporal Aspects of Illuminance:
  Illumination: quantity of the energy of the light emitted per second in all direction.

## Slide 7
(7) Continuity of Motion:
  Continuous motion to be happen if frame rate faster than 15 frame per second.
  Video motion seems smooth and achieved at only 30 frames per second, when filmed by a camera and not synthetically generated.
(8) Flicker:
  Another problem known as flicker occurs due to a periodic fluctuation of brightness perception.
(9) Temporal Aspect of Video Bandwidth:
  An important factor to determine which video bandwidth to use transmits motion video is its temporal specification.
  Temporal specification depends on the rate of the visual system to scan pixels, as well as on the human eye’s scanning capabilities.

## Slide 8: B) Transmission
Video signals are transmitted to receive through a single TV channel.
To encode colour, a video signal is a composite of three signals for transmission purpose, a video signal consists of one luminance and two chrominance signal.
The transmitter also uses the comb filter during the luminance –chrominance encoding process.
Approaches of Color encoding
  RGB signal
  YUV signal
  YIQ signal
  Composite signal
i) RGB signal:
  In the case of signal coding the color can be encoded in the RGB signal, which consists of separate signals for red, green and blue colors.

## Slide 9
ii) YUV signal:
  This signal widely used in encoding color for use in TV and video.
  The Y signal encodes the brightness information.
  The U and V signal encodes the chromatic information.
  The components division of YUV signal is:
    Y=0.3R+0.59G+0.11B
    U=(B-Y)*0.493
    V=(R-Y)*0.877
iii) YIQ signal:
The coding of YIQ signal is similar to YUV signal. The component division is slightly different.
The component division of YIQ signal is:
  Y=0.30R+0.59G+0.11B
  I=0.60R-0.28G-0.32B
  Q=0.21R-0.52G+0.31B
iv) Composite signal:
  The alternative component encoding composes all information into one signal i.e. the individual components (RGB, YUV and YIQ) must be combined into one signal.

## Slide 10: C) Digitization
Before a picture or motion video can be processed by a computer or transmitted over a computer network, it needs to be converted from analog to digital representation.
Digitization: analog to digital conversion.
Example of digitization: PCM (pulse code modulation)
Digitization consists of sampling and quantization process.
The creation of digital motion video is to digitize pictures in time and get a sequence of digital images per second that approximates analog motion video.

## Slide 11: Video File Format
  3GP
  MP4 (Moving Pictures Expert Group 4)
  FLV (Flash Video Format)

## Slide 12: Computer Based Animation
To animate something is literally to bring it to life.
An animation covers all changes that have a visual effects, visual effect can be of two major types.
  Motion dynamic: time varying positions
  Update dynamic: time varying shape, colour, texture or even lighting, camera position etc.
The visual effect is the result of exploiting the properties of human vision system.
A computer animation is an animation performed by a computer using graphical tools to provide visual effects.
Notes: Cel animation, computer animation, kinematics, morphing

## Slide 13
Basic Concepts of animation:
a) Input process:
  The first step in producing computer animation is input process.
  Key frames have to created and input into the computer.
  Key frames are the frames in which the objects being animated are at extreme or characteristic positions.
  They can be drawn using traditional artistic tools, such as pen and brush and then digitized.
b) Composition stages:
  In composition stage, the foreground and background figures are combined to generate the individual frames.

## Slide 14
c) In-between process:
  The animation of movement from one position to another need to a composition of frames with intermediate positions in between the key frames. This is called in-between process.
  This process of in-betweening is performed in computer through interpolation.
  In-betweening also involves interpolating the shapes of objects.
  Some animation involves changing the color of objects.
  In the mathematical field of numerical analysis, interpolation is a method of constructing new data points within the range of a discrete set of known data points.

## Slide 15: Animation Language
There are many different languages for describing animation and new ones are constantly being developed.
Animation languages are fall into three categories:
(1) Linear-List Notation:
  In linear-list notations for animation each event in the animation is described by a starting and ending frames numbers and an action that is to take place (event).
  Example:
  A statement such as 42, 53, B, ROTATE “PASS”, 1, 30.
  Meaning: between frames 42 and 53, rotate the object called PASS about axis 1 by 30 degrees determining the amount of rotation at each frame from table B.

## Slide 16
(2) General Purpose Language:
  Another way to describe animation is to embed an animation capability within a general-purpose programming language.
  The values of variables in the language can be used as parameters to the routines, which perform the animation.
  General purpose programming language is a programming language designed to be used for writing software in the widest variety of application domains.
    Example: C, C++, C#, Java, Visual Basic, etc.
(3) Graphical Languages:
  General animation languages describe animation in a more virtual way.
  These languages are used for expressing, editing and comprehending the simultaneous changes taking place in an animation.
  Graphical language includes various elements such as contours and lines, images, numbers, and symbols and their attributes such as movement, spatial location, color or contrast, and size.
  A high-level language and programming interface used to create graphics images.
  The major graphics languages are:
    GDI(graphics device interface), DirectX, QuickDraw, Display PDF and OpenGL. Windows uses GDI and DirectX, while the Mac uses QuickDraw and Display PDF.

## Slide 17: Transmission of Animation
Animated objects can be represented symbolically using graphical objects or scan-converted pix-map images.
The transmission of animation over computer networks may be performed using following approaches:
  Symbolic Representation
  Pix-map Representation